## Slide 1: HTJ2K
High-throughput JPEG 2000

## Slide 2
Consultant to the industry (Sandflow Consulting)
Co-chair of the JPEG 2000 activity in ISO (supported by Kakadu Software)
Involved with JPEG 2000 since the early days of D-Cinema
Dr. Pierre-Anthony Lemieux
SANDFLOW CONSULTING
pal@sandflow.com

## Slide 3: High-throughput JPEG 2000 (HTJ2K)
Published in 2019 as Rec. ITU-T T.814 | ISO/IEC 15444-15
Adds the HT block coder as an alternative to the legacy arithmetic block coder
  Built for today’s vectorized computing (CPU, GPU, FPGA…)
  Order of magnitude (10x) faster
  Approx. 5% size increase and no quality scalability
  Lossless transcoding to/from JPEG 2000 Part 1
Royalty-free

## Slide 4: Same codestream, same capabilities*
codestream
input imagery
Multi-Component and other point transforms
Spatial DWT Analysis
Quantizer
Arithmetic Block Coder
J2K Packet Generation
Multi-Component and other point transforms
Spatial DWT Analysis
Quantizer
HT Block Coder
J2K Packet Generation
HTJ2K
Legacy J2K
codestream
input imagery
* minus quality scalability
Notes: How does HTJ2K achieve these big improvements?
The answer is simple: HTJ2K merely replaces the legacy JPEG 2000 arithmetic block coder with a collection of variable-length coding schemes.
The rest of the JPEG 2000 architecture, and thus the JPEG 2000 features, remains unchanged.
The speedup comes in part because these VLC schemes are optimized for today’s vectorized computing architectures.

## Slide 5: Lossless transcoding to/from legacy J2K
Maintains compatibility with legacy JPEG 2000 applications
Provides a path to quality scalability
Legacy JPEG 2000 system
Lossless transcode
Legacy
J2K codestream
HTJ2K codestream
Efficient HTJ2K processing
Notes: For those paying attention, you might have wondered why I did not show image quality results in the previous slides.
In other words, how did we know that the speedup did not come from a significantly degradation in quality.
The answer is that mathematically lossless transcoding is available between legacy JPEG 2000 and HTJ2K, for both lossy and lossless codestreams.
This is a pretty unusual property, so let me repeat it.
It is possible to take any valid JPEG 2000 codestream, lossy or lossless, transcode it to an HTJ2K codestream, and then convert it back to JPEG 2000 without losing information.
This allows HTJ2K to be easily integrated into existing JPEG 2000 workflows, and provides a path to quality scalability.
For instance, it is possible to ingest JPEG 2000 content into a video editing station, convert it to HTJ2K to take advantage of the HTJ2K speedup during editing, and convert it back to JPEG 2000 for legacy distribution, with no impact on image quality.

## Slide 6: Lossless UHD image coding
Chart: 
| Legacy J2K | HTJ2K
Decoding speed | 2 | 67
Chart: 
| Legacy J2K | HTJ2K
Compression ratio | 2.3 | 2.2
10-second clip of Netflix' Meridian UHD SDR converted to DCDM X’Y’Z’
MacBook Pro 15-inch 2018 2.9GHz Intel Core i9 (6-core) 16GB RAM 1TB SSD
Notes: Shifting to practical applications, HTJ2K can be applied to preservation of D-Cinema assets.
The plots show the decoding speedup of HTJ2K when applied to lossless UHD content, and the impact on coding efficiency, compared to legacy JPEG 2000.
As we saw before, there is a speedup of 30x at the cost of slight decrease in coding efficiency.
The coding efficiency is around 2:1, which it typical of lossless coding of motion picture content.
These tests were run on a MacBook pro.
It is interesting to note that HTJ2K make it possible to playback the 4K lossless content in realtime on everyday PC hardware.

## Slide 7: Lossy large image coding
Chart: Decoding throughput (Mssamples/s)
| 0.5 bpp | 1.0 bpp | 2.0 bpp | 4.0 bpp
JP2 | 1028 | 724 | 424 | 217
JPH | 1804 | 1782 | 1756 | 1631
Chart: Encoding throughput (Msamples/s)
| 0.5 bpp | 1.0 bpp | 2.0 bpp | 4.0 bpp
JP2 | 428 | 318 | 205 | 131
JPH | 1960 | 1958 | 1815 | 1612
Chart: PSNR (dB)
| 0.5 bpp | 1.0 bpp | 2.0 bpp | 4.0 bpp
JP2 | 32.47 | 34.92 | 38.9 | 46.09
JPH | 32.29 | 34.62 | 38.48 | 45.53
HTJ2K
Legacy J2K
64×64 codeblocks, 9-7 wavelet transform, RGB to YCbCr irreversible decorrelating colour transform;
Kakadu SDK v8.0 on 4-core Intel i7-6700 CPU @ 3.4 GHz
Aerial photograph, 13333×13333 pixels, RGB, 8 bits per channel
Notes: Moving to the coding of large images, again comparing JPEG 2000 and HTJ2K, but this time using each codec end-to-end without attempting to transcode one into the other.
The test image is a large 170 Mpixel aerial photograph, 24-bit RGB. One characteristic of the test is that the image, due to its size, is unlikely to fit in processor caches.
Coding was lossy
The Kakadu SDK was used to generate results, running a quad-core intel processor.
The results are presented as a function of bpp.
Encoding speedup is between 4x and 10x, decoding speedup ranges from 1.75x to 7x, increasing with bitrate.
The last plot shows that, as expected, the PNSR of HTJ2K images is marginally lower than that of JPEG 2000 images at equal bitrate.

## Slide 8: Many implementations
ASIC
JS
FGPA
CPU
GPU
OpenJPH
OpenJPEG
FFMPEG
Kakadu SDK
Comprimato
OpenHTJ2K
ISO reference software
… and others
Open source and commercial
ICT-Link
grok

## Slide 9: https://demo.noproxy.cloud/
Real-time playback from a vanilla HTTP server
JavaScript decoder (OpenJPH compiled to WebAssembly)
Lossy HTJ2K essence wrapped in an MXF file
UHD image
  3840x2160
  4:2:2
  10-bit
Resolution scalability to adapt to network and CPU availability